## Slide 1
DNA sizing
Review intensity data
Adjust bin range and height of intensity for peak detection
Confirmation
Manually genotype calling by PGx experts
Exporting result
Proposed cloud system
DNA sizing
Plot intensity data
Adjust bin range and height of intensity for peak detection
Confirmation
Genotype calling
Genotype calling result
Feature process (generate report)
Manually
upload
Manually input
Quality controls
Current approach
FSA files
Upload
PGx: Pharmacogenomics
FSA: Fragment Sequence Analysis
Proposed cloud system
Provide an integration system from peak detection to report generation.
Prevent human bias
Improve efficiency
Improve management
Transparent
Current approach
Web application
Separate systems, software, requires some manual steps
High risk of human bias
Low efficiency because of system separation.
Hard to check history
Difficult to manage
Genotype calling (KIT)
Feature process (generate report)
GeneMapper Software

## Slide 2: Reference peak detection
Data:
101 samples (202 FSA files)
Reference: GeneScan 120LIZ
Parameters: Minimum intensity: 300
Result:
We could detect all reference peaks of all 202 FSA files.
DNA sizing model of each FSA file was built based on corresponding detected reference peaks
R square: 0.999863 ± 0.000011
Reference sizes (bp) | Data points (cycles) |  |  | Intensity |  | 
 | Median | Min | Max | Median | Min | Max
15 | 756 | 619 | 973 | 1854 | 416 | 9643
20 | 806 | 667 | 1025 | 1973 | 383 | 9549
25 | 846 | 703 | 1067 | 2409 | 353 | 8146
35 | 934 | 788 | 1157 | 2424 | 392 | 9088
50 | 1077 | 925 | 1307 | 2992 | 372 | 8796
62 | 1215 | 1056 | 1451 | 2882 | 423 | 9270
80 | 1395 | 1228 | 1636 | 2786 | 358 | 8023
110 | 1732 | 1549 | 1983 | 2984 | 390 | 8828
120 | 1841 | 1654 | 2094 | 3022 | 393 | 8906

## Slide 3: Example of calling process
Default minimum intensity was as 1000; some of marker could not be detected
After adjust intensity, these markers was identified:
*10B/*10B

## Slide 4
A
B
C
D

## Slide 5
FSA files
PGx: Pharmacogenomics
FSA: Fragment Sequence Analysis
Proposed cloud system
Provide an integration system from peak detection to report generation.
Prevent human bias
Improve efficiency
Improve management
Transparent
Current approach
Proposed cloud system
Estimate DNA size
Plot intensity data
Review and adjust DNA size and intensity to detect target peaks
Star-allele calling
Confirm called results
Generate reports
Quality control and confirm
Web application
Separate systems, software, requires some manual steps
High risk of human bias
Low efficiency because of system separation.
Hard to check history
Difficult to manage
Estimate DNA size
Plot intensity data
Review and adjust DNA size and intensity to detect target peaks
Confirmation
Manually genotype calling by PGx experts
Exporting result
Manually
upload
Manually input
Current approach
Third party star-allele calling tools
Generate reports
GeneMapper Software
Upload
A
B

## Slide 6: Example of calling process
Default minimum intensity was as 1000; some of marker could not be detected
After adjust intensity, these markers was identified:
*10B/*10B